## Slide 1: Is this seat taken?: A multi-faceted study to Inform Chicago Transit Authority’s Future Rail Car seating design
Transport Chicago
2014
Maulik Vaishnav
Chicago Transit Authority
Resource Planner
Tara O’Malley
Chicago Transit Authority
Coordinator, Market Research

## Slide 2: Background
Growing transit agency interest in railcar design across the country.
  BART – New Train Car Project
  WMATA – 7000 Series
  MBTA – Red Max
  NY MTA – Off Peak
  CTA – MAX, 7000 Series
Theoretical Railcar Capacity Research
  Crowded Scenario Standee Space – as small as 2.15 sq ft/person
  5.4 sq ft per transverse seat (forward or backward facing)
  4.3 sq ft per longitudinal seat (aisle facing)

## Slide 3: STUDY Background
CTA operated cars with only transverse seating (front or back facing seats) until the recent introduction of new railcars.
The new 5000 series cars feature longitudinal (aisle-facing) seats.
An opportunity to compare both seating styles with customer feedback, observations, and rail car performance analysis
Focus on busy lines in peak periods and included the older 2400/2600 series, 3200 series, and 5000 series cars.

## Slide 4: Current Car layouts
Lots of Seats Narrow Aisle Limited Standing
Support
Staggered 2x1 Seating ADA spot Poles
Longitudinal Seating 2 ADA spots Horizontal Standing
Support

## Slide 5: Methodologies
Observations
  Dwell time analysis
    Observed via surveillance video at various stations
  Capacity
    Observed onboard individual rail cars
Customer Survey Research
  Online
  Intercept on the platform

## Slide 6: Dwell Time Methodology
Goal is to determine performance differences among rail car types
Stations were selected based on loading and boarding similarities
Observations were conducted in the peak periods
Control for anomalies
  Accommodate cases where trains may have been held for delays (signal, operator, etc.,)
  Highest 10 percent and lowest 10 percent of observations were removed

## Slide 7: Dwell Time Analysis
Chart: Train Car Type
| 2000s | 3000s | 5000s
Bottom | 12.65 | 12.9 | 13.5
2Q Box | 3.1 | 2 | 3.05
3Q Box | 3.775 | 3.5 | 3.3
Mean | 16.3511 | 15.6761 | 17.0848

## Slide 8: Capacity
2400/2600 Series
  Theory: 84-102
  Observed: 108
3200 Series
  Theory: 94-116
  Observed: 108
5000 Series
  Theory: 106-134
  Observed: 101

## Slide 9
Photo Courtesy of Clint McMahon aka “minniepixel” via Flickr
2400/2600 SERIES

## Slide 10
3200 SERIES

## Slide 11
5000 SERIES

## Slide 12: Customer Preferences
Chart: 
| Straps | Back of Seat | No Preference | Lean | Pole
Stabilizing Element Preference | 0.03 | 0.03 | 0.09 | 0.31 | 0.54
Chart: Seating/Standing Preference
Prefer to Sit | 0.84
Don’t have a preference | 0.11
Prefer to Stand | 0.05
Chart: Rail Car Choice
| 2400/2600 Series | 3200 Series | 5000 Series
Best Seating | 0.306 | 0.47 | 0.224
Best Rail Car Overall | 0.309 | 0.467 | 0.225

## Slide 13: 7000 Series recommendations
Incorporate each car’s benefits in one layout: “A little something for everyone”
Begin with the 3200 series style in the center of the car
Prioritize safety in front: arrange seats facing the center on the cab end of the car
Maximize seats on non-cab end: arrange seats in a two-by-two fashion
Include stabilization elements similar to the new cars

## Slide 14: 7000 series RECOMMENDATIONS (37 Seats)
Staggered seats like the 3200
Two-by-two seats on non-cab end to maximize number of seats
Fewer weather panels will help customers move to the center of the car
Center-facing seats offer “safer” position in the rail car for customers

## Slide 15: Questions?